## Slide 1: Progress Mälaren – 1D modelling
1D models of 5 basins
  Sequential runs; surface outflow of one basin is used as inflow for the next
Aim: Selmaprotbas calibration, maybe also used for scenarios
ISIMIP forcing data, 1995-2015
GOTM-Selmaprotbas settings
  Hourly time step
  0.5 m layers
  3 phytoplankton, 1 zooplankton group
Final version: GWLF inflows driven by same meteorology
E & F
together

## Slide 2: Progress Mälaren – 1D modelling
YAML templates and GOTM-SP.exe/
Compile meteo data.R
ISIMIP data/
Compile hypsograph data.R
Compiled data/
Inflow data/
Set up GOTM-SP runs.R
Compile stream data.R
Simulation folder/
Run GOTM-SP for basins.R
helpers/ create_inflow_files_from_basin_outflow.R
helpers/modify_stream_sections_gotm_yaml.R
output.nc files
Streams: using discharge from HYPE model from earlier studies
  Nutrient concentrations are constant
GSWP3-W5E5 ISIMIP bias-adjusted climate data
Hypsograph extrapolated from Sonesten et al. (2013)
Compiled latest GOTM lake-branch version with Selmaprotbas
Basin exchange resolved during runs

## Slide 3: Progress Mälaren – 1D modelling
I have not yet compared with observations
Temperature and PO4 look realistic
O2 and NO3 do not
Phytoplankton is growing (up to 10 mg-Chl/m3)
Temperature
Oxygen
Phosphate
Chlorophyll
0m
60m